Suspension and Spring Specification - VW Golf Mk5,6&7

- The Forge Motorsport suspension gives you the best balance between performance & comfort.

- With 32 levels of dampening adjustability the suspension kit can be set to any preference, for track or street driving, and adjust both bump and rebound at the same time

- Pillow ball top mounts on the front shocks in order to dial out excessive camber

- Manufactured from carbon steel 52mm diameter seamless tube (to JIS G3445 and DIN2393).

- A 44mm linear characteristic internal piston provides the best dampening response for the tube diameter.

- High quality mono tube shock design

- The high viscosity oil used in the damper ensures the very best and most efficient shock-absorbing action.

- The length of the shock can be adjusted, preventing the need to adjust the spring perch like on a normal coil-over, and so offering the maximum shock-absorbing travel.

- Cold drawn springs are manufactured from high strength steel (to SAE9252).

- Spring rates of 8kg/mm (front) and 4.5kg/mm (rear) for Golf Mk5,6&7

The Forge Suspension System has been developed with fast road and track driving in mind, but for those that prefer more show than go, it also offers a two stage lowering system that takes your car from low to really low !

Firstly the shock body itself is adjustable in length which means that you don’t have to make the spring shorter in order to lower the car. This means that ride quality can be maintained as the spring stays at its optimum length and the travel of the shock (i.e. its ability to absorb bumps) isn’t affected. On the Golf Mk5&6 platform we suggest lowering up to 45mm front and 35mm rear, for Golf Mk7 we recommend up to 45mm front and 50mm rear. This makes it perfect for track use where a lower centre of gravity is desireable, but also doesn’t make the ride overly hard.

Secondly the length of the spring can be adjusted, just like a normal coilover, so as the spring gets shorter the car gets lower.

This does also mean that if the shock is adjusted AND the spring platform adjusted at the same time, you can obtain huge drops over stock but you will need supporting modifications in order to run a regular road car this low, along the lines of fully adjustable control arms, and possibly chassis modifications, so that your camber, caster and toe settings can stay as close to factory settings as possible. This is really only recommended for show purposes.